MIDI INTERFACE LIBRARY				       3-02-88

















		  MIDI BOARD APPLICATION PROGRAM INTERFACE

			       Dave Tutelman













































     MIDI INTERFACE LIBRARY				       3-02-88

				  CONTENTS




       1.  REQUIREMENTS

       2.  ARCHITECTURE	 -  the	 specification of the functions	calls.
		 (No implementation detail, but	serious	 attention  to
		 implementation-independence).

       3.  IMPLEMENTATION  - sample for	an MS-DOS PC and the BYTE MIDI
		 board.

       4.  BIOS	FUNCTIONS - specific to	the implementation in  Section
		 3.

       5.  PASCAL FUNCTIONS - it also works in Turbo Pascal.

       6.  FUTURE DIRECTIONS












































     MIDI INTERFACE LIBRARY				       2-21-88


			      1.  REQUIREMENTS



     Portability

     There is a	need for a library of function calls to	control	a MIDI
     interface board.  The major requirement on	the library is that it
     permit a high degree of portability of the	applications that use
     it. Note that we are not requiring	a portable implementation of
     the library, just portability of the interface. Thus, each	of us
     who implements the	library	for his	or her local system, is	able
     to	use application	software that any of us	writes.	(This is
     worst-case, of course. There must be tens or hundreds of each
     local system that could share implementations of the library.)

     To	achieve	the goal of portable applications, the dimensions of
     portability should	include:

	- Boards: different boards have	different hardware interfaces,
	  and even significant differences in capability. This
	  interface must allow "smart" boards to make use of their
	  additional capability; however, the capabilities must	be
	  sufficiently "abstracted" to allow their implementation in
	  software for boards that are just "dumb UARTs".

	- Synthesizers:	different manufacturers	(and even different
	  models from the same manufacturer) have different MIDI
	  implementations. The interface library, if it	recognizes the
	  MIDI protocol	at all,	should be usable for all synths. This
	  means	that it	must either (1)	stick to the common portion of
	  the MIDI spec	used by	all manufacturers, or (2) be
	  externally customizable for any manufacturer's
	  implementation.

	- Compilers: different C compilers have	different ways of
	  getting at system and	hardware functions. The	library	should
	  be callable from any of the common C compilers, though its
	  implementation could be different for	each.

	- Computers: the above,	of course, should extend to compilers
	  for different	computers. C is	a portable language, and the
	  function calls should	be implementable across	a variety of
	  computers.

	- Languages: this is a personal	hobby-horse, not a real
	  requirement. My son programs in Turbo	Pascal,	not C. I'd
	  like a library that could be easily "redefined" and
	  re-implemented for Pascal.

     The value of portability is that we could share application
     software even though we have different computers, MIDI boards, or
     compilers.	With careful programming, it might even	be possible to
     share software across synths (easy	for a sequencer, harder	for a
     patch librarian, still harder for a patch editor).



				Page  1	- 1




     MIDI INTERFACE LIBRARY				       2-21-88


     Efficiency

     The library must be implementable with efficiency across a
     sizable majority of the portability range.	If the implementations
     are inefficient, then the library won't be	used by	application
     developers. While the definition of the library functions can't
     guarantee an efficient implementation, it can guarantee an
     inefficient implementation. (A good example of a "standard"
     abstraction that nobody uses because it's too inefficient is the
     set of Comm Port BIOS functions in	MS-DOS.	 The definition	of the
     functions makes it	impossible to provide an implementation	that
     an	application could use efficiently.)

     The aspects of efficiency that are	required are:

	- Real-time efficiency.	This strongly drives for an autonomous
	  handler (interrupt-driven or on-board	processing) to handle
	  the MIDI line	itself.	It also	argues against unnecessary
	  moving of bytes.

	- Efficient use	by the application. This implies that function
	  calls	must be	provide	the application	information about MIDI
	  messages. The	requirement is certainly not met if the
	  application has to baby-sit the transmission and reception
	  of each MIDI byte.

	- Efficient use	of on-board hardware. MIDI interfaces exist
	  that provide on-board	parsing	of the MIDI byte stream	into
	  messages, and	on-board timers	and timestamping. An interface
	  that ignores these functions requires	that the application
	  duplicate them in software, rendering	the library
	  inefficient for those	boards.	Thus the library functions
	  must provide abstractions for	message	(not just byte)
	  handling and timestamping; the abstractions must allow for
	  efficient use	of on-board hardware where it exists, but be
	  software-implementable for the "dumb UART" board.

     What follows is a proposal	for such a library. It assumes that
     the functions would be coded close	to the machine (probably,
     though not	necessarily, in	assembler), but	callable by the
     standard C	calling	conventions. The interface is more than	a
     "dumb UART" interface; it uses interrupt-driven RAM buffering,
     and includes a timestamp facility.	If your	board includes these,
     then it should be easy to implement the functions;	if not,	then
     they must be implemented in software. Attention has been given to
     return codes that indicate	the limitations	of a capability; they
     should make it possible to	write portable applications that adapt
     to	the limitations	of the local implementation.










				Page  1	- 2




     MIDI INTERFACE LIBRARY				       2-08-88


			      2.  ARCHITECTURE


     The library provides two (related)	services:
	- Sending and receiving	MIDI signals.
	- Timing, both to timestamp received MIDI signals and to
	  provide "current time" to the	program.

     Both look to the application program as if	there is autonomous
     hardware providing	the service, though it may well	be implemented
     in	software. For instance:
	- The Roland MPU-401 has an on-board processor that handles
	  lots of the functionality, removing the burden from your
	  computer's CPU. The implementation for the MPU-401 would be
	  little more than a set of I/O	functions.
	- The BYTE MIDI	board (Jay Kubicky, BYTE Magazine, June	1986)
	  has an on-board timer	chip, but only a dumb UART and no
	  processor. The implementation	code to	handle the timing
	  functions would therefore be pretty simple, but the
	  send/receive code would have to respond to hardware
	  interrupts, handle buffering,	parse the MIDI messages, etc.
	- A MIDI interface hacked together with	no timer chip would
	  have to use the computer's own timer to derive its
	  timestamps.

     I believe this is feasible, at an acceptable performance penalty,
     for many computers. (Just for reference, I	built the BYTE board,
     as	did several of my co-workers. I	intend to implement the
     library for the BYTE board, as a sanity check of the proposal.)

     All the functions deal with "returned values" as parameter
     pointers; the actual return value of the function is reserved for
     the function's exit code. This convention,	while not in the
     original spirit of	"C", permits a uniformity of calling structure
     and seems to be spreading in the industry (note, for instance,
     the Application Program Interface specs for Microsoft's new LAN
     or	Windows	products).


     Send/Receive Functions

     There are functions to send and receive both single bytes and
     full MIDI messages. No attempt is made in the library to parse
     the message, beyond just determining its beginning	and end. (Of
     course, it	must handle system-exclusive messages.)

     There is a	buffer in the library to store bytes received from the
     MIDI line that have not been requested yet	by the application,
     and to store bytes	sent by	the application	until they can be
     output to the MIDI	line. Interaction between the buffer and the
     MIDI line is invisible to the application program;	it could, for
     instance, be implemented in an interrupt handler (or, in the case
     of	the MPU-401, be	handled	by the on-board	processor).

     This was the most difficult decision in the architecture.
     Cognizant of the inefficiencies in	storage	(buffer	both in	the


				Page  2	- 1




     MIDI INTERFACE LIBRARY				       2-08-88


     library and in the	application) and real-time (need to move bytes
     between the buffers), I worked for	a while	with a design that
     used a buffer allocated and owned by the application, which was
     shared with the library. The interface became considerably	more
     complex for the application programmer, and required an
     undesirable sharing of implementation imformation.	I eventually
     dropped this approach as not being	worth the gain in efficiency.

     The functions are:



     Send MIDI Byte

     int midi_putc ( b )

     unsigned char   b;	     /*	byte to	be sent	*/

     Put a byte	in the transmit	buffer to be sent out on the MIDI
     line.

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Transmit buffer full. Nothing was sent, but system is
		 still sane.
       -1	 Miscellaneous error.


     Receive MIDI Byte

     int midi_getc ( bp, tp )

     unsigned char   *bp;    /*	pointer	to byte	received */
     unsigned int    *tp;    /*	pointer	to timestamp */

     Get a byte	from the receive buffer, and the associated timestamp.
     (Note that	the timestamp is associated with the message in	which
     the byte was received, and	may not	be the exact time that this
     byte was received.)

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Receive buffer	overflowed. No guarantee of sanity of
		 anything hereafter, unless "initialize" is called
		 again.
       +3	 Receive buffer	empty. Ignore contents of *bp.
       -1	 Miscellaneous error.


     Send MIDI Message

     int midi_putmsg ( buf, bufsize, xmtsize )

     unsigned char   *buf;	     /*	string of bytes	*/
     int	      bufsize;	     /*	number of bytes	to send	*/
     int	     *xmtsize;	     /*	number of bytes	actually sent */


				Page  2	- 2




     MIDI INTERFACE LIBRARY				       2-08-88


     Put the string of bytes in	the transmit buffer, to	be sent	to the
     MIDI line.	Exactly	"bufsize" bytes	are sent (if there is room in
     the transmit buffer); no attempt is made to assure	that the
     string is a legal MIDI message. If	there isn't enough room	for
     "bufsize" bytes in	the transmit buffer, then fewer	bytes are
     transmitted, that number being returned in	"xmtsize". The
     remaining bytes must be re-sent, in a subsequent call to
     midi_putmsg().

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Transmit buffer full. See "xmtsize" for number	of
		 bytes accepted	for transmission.
       -1	 Miscellaneous error.


     Receive MIDI Message

     int midi_getmsg ( buf, bufsiz, rcvsize, timestamp )

     unsigned char   *buf;	     /*	application buffer to store message */
     int	      bufsize;	     /*	maximum	size of	buffer */
     int	     *rcvsize;	     /*	actual number of bytes transferred */
     unsigned int    *timestamp;     /*	time message came off MIDI line	*/

     Gets the next message from	the receive buffer (if there is	one),
     together with its timestamp. Normally, a complete message will be
     transferred to the	application buffer. However:
	- If the message is longer than	the buffer, then the buffer
	  will be filled with the partial message.
	- If a reasonable chunk	of a system-exclusive message is in
	  the receive buffer, then that	chunk will be transferred.
	  (Note	that, in general, you don't know the length of a
	  system-exclusive message until you receive its last byte, or
	  even the first byte of the next message.)
     In	each case, the next midi_getmsg() or midi_getc() will begin
     with the next unread byte.	In this	way, a very long message can
     be	read in	parts.

     Note that "rcvsize" contains the actual number of bytes
     transferred. It is	a byte string, not a character string. That
     is, it's not null-terminated; embedded nulls are quite legal, and
     the library doesn't append	a null at the end. You must use
     "rcvsize" to find the end of the string reliably.

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Receive buffer	overflowed. No guarantee of sanity of
		 anything hereafter, unless "initialize" is called
		 again.
       +3	 Receive buffer	empty. Ignore contents of application
		 buffer.
       +4	 Application buffer not	big enough to hold message.
		 More to read.
       +5	 Part of a system-exclusive message transferred. More
		 to read, though it may	not have been received yet.


				Page  2	- 3




     MIDI INTERFACE LIBRARY				       2-08-88


       -1	 Miscellaneous error.


     Ignore Received Message

     (To be added.) Actually, two different approaches to "filtering"
     are under consideration.

	- A function midi_abort	(), which throws away the rest of the
	  last message whose status byte was transferred. This allows
	  the application to filter based on reading only short
	  messages, and	not being bothered with	the rest of long,
	  uninteresting	messages.
	- A function midi_filtable (), which maintains a table of
	  status bytes that the	library	uses to	filter received	MIDI
	  messages.
     Comments on the choice (or	dumping	it altogether, since
     application-level filtering is quite feasible without either
     function) are welcome. In any event, this woun't be in my first
     implementation.


     Timer Functions

     The timer is the keeper of	an unsigned integer, whose value is a
     number of mini-beats. (A mini-beat	is the smallest	interval of
     resolution	that is	"interesting" to the application. It might be,
     for instance, one sixteenth of a beat for a reasonably
     time-quantized sequencer.)	Setting	the length of a	mini-beat is
     tantamount	to setting the tempo.

     The integer in the	timer is the value timestamped on MIDI
     messages, and the value returned by a "get-time" function call.
     The value of a timestamp on a MIDI	message	is the time at which
     the first byte of the message arrived. Only one timestamp need be
     kept per message; the timestamp returned by a "receive-byte"
     function call is that of the message, not necessarily the
     individual	byte.

     Since implementations of the timer	will vary widely, the
     resolution	and maximum count will probably	vary too. For that
     reason, the "set-tempo" function call returns an indication of
     the maximum count that can	be reliably handled by the timer at
     that tempo. No guarantee is made as to the	sanity of larger
     numbers. A	"set-time" function is available for the application
     to	controllably clear the timer before it "overflows".

     The "set-tempo" function can also be used to indicate that
     timestamps	aren't interesting to the application. Some
     implementations of	the library may	use this indication to be more
     efficient with real time or memory. If this feature is used, the
     timestamps	returned by the	receive	functions will be junk values.

     The functions are:




				Page  2	- 4




     MIDI INTERFACE LIBRARY				       2-08-88


     Set Tempo

     int midi_settempo ( speed,	maxcount )

     unsigned int     speed;	     /*	number of mini-beats per minute	*/
     unsigned int    *maxcount;	     /*	maximum	reliable timestamp */

     Accepts a tempo (speed) to	increment the timer. The tempo is in
     mini-beats	per minute. Examples:
	- If the song's	tempo is 100 beats (quarter notes) per minute,
	  and the desired resolution is	a 32nd note, that gives	32/4 *
	  100 =	800 mini-beats per minute. Each	count in the timer
	  represents a 32nd note at the	given tempo.
	- If a song's tempo is 60 beats	per minute, and	the program
	  also synchronizes a drum machine, then we must be clocked at
	  some integer multiple	of 24 pulses per quarter note. That
	  gives	60 * 24	= 1440 mini-beats per minute (or some multiple
	  thereof, if the application requires).

     The library leaves	in "maxcount" the largest number that can be
     trusted as	a timestamp at the requested speed. It is up to	the
     application program to see	that the timer is reset	before it
     reaches this value.

     There is no assurance of the value	in the timer immediately after
     setting the tempo.

     If	the function is	called with speed=0, then timestamps are
     "uninteresting" to	the application. The library is	free to	use
     this fact to more efficiently use the resources of	the machine,
     and to fail to return timestamps to the application.

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Timer service not supported.
       +3	 Tempo outside supported range.
       -1	 Miscellaneous error.


     Set Time

     int midi_settime (	t )

     unsigned int    t;	     /*	force this value into the timer	*/

     The timer is reset	to "t",	and timing continues at	the same
     tempo. It is required that	"t" not	exceed "maxcount", the maximum
     reliable value in the timer.

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Timer service not supported.
       +3	 Value outside supported range.
       -1	 Miscellaneous error.




				Page  2	- 5




     MIDI INTERFACE LIBRARY				       2-08-88


     Get Time

     int midi_gettime (	t )

     unsigned int    *t;     /*	value currently	in the timer */

     This is useful for	timing output. (Wait until the timer reaches
     the desired value,	then crank out the notes associated with that
     clock pulse.)

     [An alternative design, which I discarded,	would be to associate
     timestamps	with the transmitted messages in the same way we do
     with received messages. While conceptually	elegant, it would have
     made implementation much harder. Consider,	for example,
     implementing this feature with a board whose timer	didn't include
     a hardware	interrupt.]

     unsigned int    *t;     /*	current	value in timer */

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       +2	 Timer service not supported.
       -1	 Miscellaneous error.


     Housekeeping Functions

     The library contains functions to initiate	and terminate use of
     the MIDI interface. These functions (especially terminate)	may do
     nothing, but they may be quite busy, again	depending on the
     implementation. For instance, the "initialize" function may hook
     an	interrupt vector (and the "terminate" function release it).

     However, there are	some specific, application-visible effects of
     the "initialize" function:
	- The transmit and receive buffers are cleared.
	- The state machine that parses	MIDI messages is cleared;
	  after	an "initialize", it tries to sync on bytes from	the
	  MIDI line to find the	beginning of a new message.
	- The timer is "turned off"; that is, tempo and	timer values
	  are meaningless after	an "initialize".

     It	is good	practice to be sure that "terminate" is	called when
     the application program exits, even an abnormal exit. The library
     implementation may	hook interrupts	and do things to the hardware
     that need to be undone if your computer is	to remain sane after
     the application goes away.

     The functions are:









				Page  2	- 6




     MIDI INTERFACE LIBRARY				       2-08-88


     Initialize	MIDI Interface

     int midi_init ( )

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library is already installed. Only partial
		 initialization	was necessary.
       -1	 Miscellaneous error.


     Terminate MIDI Interface

     int midi_end ( )

     Returns 0 if successful.  Other returns include:
       +1	 MIDI library not initialized.
       -1	 Miscellaneous error.









































				Page  2	- 7




     MIDI INTERFACE LIBRARY				       3-02-88


			  3.  IMPLEMENTATION NOTES

     This section describes a possible implementation of the MIDI
     library specified in the previous section.	The particular
     implementation is for an AT&T PC6300 computer (an XT-like MS-DOS
     machine) with a BYTE MIDI board (from the article by Jay Kubicky
     in	the June 1986 issue of BYTE). The board	hardware is a "dumb
     UART" plus	a counter-timer.



     Structure

     My	decision was to	implement the library as a collection of
     "BIOS" functions. That is,	I built	a Terminate-and-Stay-Resident
     program (a	"TSR") that hooks interrupt 79H	and implements each
     library function as a subfunction on that software	interrupt. (I
     chose Int 79H because nothing I know of uses it; the choice is
     basically arbitrary.)

     The intermediate step of an INT call has its pluses and minuses.
     Advantages:
	- Easily interfaced to a variety of languages. Just about
	  every	language implementation	for MS-DOS computers has an
	  efficient mechanism to call BIOS functions, so the library
	  itself is just a series of "setup registers and INT 79H"
	  operations.
	- Doesn't take up storage in small model applications. The
	  driver lives in its own segment.
	- Won't	crash PC if application	aborts.	A disorderly
	  termination of an application	will leave the hardware
	  interrupt for	the MIDI board still enabled. A	subsequent
	  received MIDI	byte could easily hang the machine, if the
	  interrupt handler were gone with the application. But	the
	  use of a TSR means that the interrupt	handler	can continue
	  to field hardware interrupts even after the application is
	  history.
     And disadvantages:
	- Lost efficiency at Application Program Interface. There is
	  some overhead	involved in fielding the software interrupt
	  and determining which	function to call.
	- Uses machine storage,	even when MIDI app not running.	The
	  driver is under 3K, so this is not much of a factor on a
	  half Meg machine. 3K is, however, a visible fraction of a
	  64K segment, so the TSR does save space for small model
	  applications (as noted under "advantages").

     I'm implementing the function calls for Turbo C and Turbo Pascal.
     Others, including assembler, are very easy	to build; just set up
     the registers and do an INT 79.








				Page  3	- 1




     MIDI INTERFACE LIBRARY				       3-02-88


     Calling Hierarchy

     Here are the functions internal to	the implementation, presented
     as	a "call	tree". I haven't bothered to "merge" trees for common
     sub-functions, because only three functions are called from more
     than one place. (Those functions are HardXmt, HardGetTime,	and
     TbufOut.) Included	with each function is the name of the .ASM
     file where	its code can be	found. Note that almost	all
     dependencies on the hardware specifics of the board have been
     kept in HARDWARE.ASM. The rest of the files contain code that can
     be	largely	reused for any "dumb-UART" MIDI	board.

     START			MIDIBIOS.ASM  The "main" program.
	 install		MIDIBIOS.ASM  Plug interrupt vectors.


     BiosEntry			MIDIBIOS.ASM  Int 79H entry point.
	 Init			MIDIBIOS.ASM
	     TxrxInit		TXRX.ASM      Initialize transmit/rcv.
	     TimerInit		TIMER.ASM
	     HardInit		HARDWARE.ASM
	 Term			MIDIBIOS.ASM
	     TxrxTerm		TXRX.ASM
	     TimerTerm		TIMER.ASM
	     HardTerm		HARDWARE.ASM
	 Putb			TXRX.ASM
	     HardXmt		HARDWARE.ASM
		 TbufOut	TXRX.ASM
	 Putm			TXRX.ASM
	     HardXmt		(see above)
		 TbufOut	(see above)
	 Getb			TXRX.ASM
	 Getm			TXRX.ASM
	 Setempo		TIMER.ASM
	     HardTempo		HARDWARE.ASM
	 Setime			TIMER.ASM
	     HardSetTime	HARDWARE.ASM
	 Getime			TIMER.ASM
	     HardGetTime	HARDWARE.ASM


     HardInt			HARDWARE.ASM  Hardware interrupt entry.
	 RbufIn			TXRX.ASM
	     newstate		STATES.ASM    State machine for	protocol.
	     HardGetTime	(see above)
	 TbufOut		(see above)



     Internal Buffer Structure

     The library itself	keeps a	transmit and a receive buffer. (In my
     first cut each is 256 bytes long, but that's a defined constant
     and can be	"tuned".) Each is a circular buffer with and "in"
     pointer and an "out" pointer. The receive buffer is different in
     that it has some internal structure.


				Page  3	- 2




     MIDI INTERFACE LIBRARY				       3-02-88


     The driver	must parse the MIDI message in order to	find where new
     messages begin. (It needs to know this as the bytes come in, so
     it	can record the timestamp.) We store the	timestamp right	in the
     received data buffer (as two consecutive bytes), along with a
     "cut mark"	that delimits the messages. (The cut mark is a byte
     that is illegal in	the MIDI protocol.) This gives a three-byte
     overhead for each message in the receive buffer. (This is more
     than a 50%	overhead for the typical sequencer application,	but
     most of it	is necessary; the timestamps have to be	stored
     somewhere.)



     MIDI Message Parsing

     As	noted above, the MIDI message must be parsed (at least to
     delimit messages) as the bytes are	put in the driver's buffer.
     This implies that the parsing must	take place at the hardware
     interrupt level, where it has to be very speedy. We do this by
     constructing a state table	of the MIDI protocol that can delimit
     messages in about 15 machine instructions.

     The state table has 7 rows	(states) and seven columns (input
     classes), as follows:
     STATES
       INIT	 "Initial" state, looking for status byte.
       RS1	 In this state,	we'll accept status byte or "running
		 status", where	last message had one data byte.
       RS2	 Same as RS1, but last message had two data bytes.
       ONE1	 Looking for lone data byte of message.
       ONE2	 Looking for first of two data bytes.
       TWO2	 Looking for second of two data	bytes.
       SYSEX	 Looking for EOX at the	end of a system-exclusive
		 message.

     and INPUT CLASSES
       DATA	 Data byte, beginning with a 0-bit.
       GET1	 Status	byte of	a one-data-byte	message.
       GET2	 Status	byte of	a two-data-byte	message.
       GET0	 Status-byte-only message.
       SYSEX	 Status	byte of	a system-exclusive message.
       EOX	 Terminal byte of a system-exclusive message.
       ERROR	 Unassigned status byte	- should never happen.

     The table that we get as a	synthesis of the states	and input
     classes (less the "ERROR" column) is shown	below. A "hyphen"
     entry denotes a MIDI protocol error, and goes to the initial
     state but also flags the message as erroneous. An asterisk	(*)
     indicates that the	input byte is the start	of a new message.
     (Indeed, this is the primary output of the	state machine, since
     the point is to delimit MIDI messages.) A pound sign (#) is
     another output indicator; it means	that we	know this byte is the
     last in the current message. (We can't always tell	the last byte
     before the	start of the next message, but we can do useful	things
     when we do	recognize it.)



				Page  3	- 3




     MIDI INTERFACE LIBRARY				       3-02-88


		     DATA    GET1    GET2    GET0    SYSEX   EOX
     ------------------------------------------------------------


     INIT	      -	     ONE1*   ONE2*   INIT*#  SYSEX*  INIT#


     RS1	     RS1*#   ONE1*   ONE2*   INIT*#  SYSEX*  INIT#


     RS2	     TWO2*   ONE1*   ONE2*   INIT*#  SYSEX*  INIT#


     ONE1	     RS1#     -	      -	      -	       -      -


     ONE2	     TWO2     -	      -	      -	       -      -


     TWO2	     RS2#     -	      -	      -	       -      -


     SYSEX	     SYSEX   ONE1*   ONE2*   INIT*#  SYSEX*  INIT#
     ------------------------------------------------------------



     Counter-Timer

     The timing	functions use the 8253 counter-timer chip on the MIDI
     board. Since the 8253 has several counters	on the chip, one can
     be	used to	set the	tempo and feed its ouput to another which
     keeps the timestamp. The first, or	tempo, timer counts down a 2
     MHz clock by a ratio that can be set between 1 and	64K. The
     countdown ratio defines the tempo (in mini-beats),	and the
     second, or	timestamp, timer counts	those beats. Note that this
     gives about 1800 mini-beats per minute (40	beats per minutes at
     48	mini-beats per beat) as	the slowest tempo supported by the
     board itself; I will get around to	modifying the driver to	do the
     bookkeeping for slower tempos.

     Most of the obscurities in	the code are checks to make sure that
     we	won't get a "divide overflow" error when computing the
     countdown ratio for a given tempo.	Everything else	about the
     timing functions are pretty straight-forward.













				Page  3	- 4




     MIDI INTERFACE LIBRARY				       1-25-88


			     4.	 BIOS FUNCTIONS


     The assembly-language portion of my implementation, as discussed
     in	Section	3, is a	collection of "BIOS" functions for handling a
     MIDI interface. The BIOS is currently called through Int 79
     (Hex), but	the specific interrupt used is a defined constant in
     the header	file. The function calls are made, in BIOS fashion, by
     setting the registers appropriately (starting with	the function
     number in AH) and issuing the instruction INT 79h.

     The MIDI BIOS functions are one-to-one with the C functions.
     Refer to the corresponding	C functions in Section 2 for
     explanations of the functions; only the register syntax is	given
     in	this section. Note that	the return codes (in the AL register)
     are the same as the returned values for the C functions, with one
     addition: calling a nonexistent function returns -2.

     The functions are:



     Function 0	- Initialize MIDI Interface

     On	Call:
       AH	 Function code 0.

     On	Return:
       AL	 Return	code.



     Function 1	- Terminate MIDI Interface

     On	Call:
       AH	 Function code 1.

     On	Return:
       AL	 Return	code.



     Function 2	- Send MIDI Byte

     On	Call:
       AH	 Function code 2.
       AL	 Byte to be sent.

     On	Return:
       AL	 Return	code.








				Page  4	- 1




     MIDI INTERFACE LIBRARY				       1-25-88


     Function 3	- Receive MIDI Byte

     On	Call:
       AH	 Function code 3.
       DS:BX	 Pointer to byte memory	to store received byte.

     On	Return:
       AL	 Return	code.
       DS:[BX]	 Received byte.
       DX	 Unsigned 16-bit timestamp.



     Function 4	- Send MIDI Message

     On	Call:
       AH	 Function code 4.
       DS:BX	 Pointer to byte string	to transmit.
       CX	 Number	of bytes to send.

     On	Return:
       AL	 Return	code.
       CX	 Number	of bytes actually sent.



     Function 5	- Receive MIDI Message

     On	Call:
       AH	 Function code 5.
       DS:BX	 Pointer to memory to put received byte	string.
       CX	 Maximum number	of bytes to transfer.

     On	Return:
       AL	 Return	code.
       CX	 Number	of bytes actually transferred.
       DX	 Unsigned 16-bit timestamp.



     Function 8	- Set Tempo

     On	Call:
       AH	 Function code 8.
       DX	 Unsigned 16-bit tempo in mini-beats per minute.

     On	Return:
       AL	 Return	code.
       DX	 Unsigned 16-bit "maxcount". (Always 0FFFFh in my
		 implementation.)








				Page  4	- 2




     MIDI INTERFACE LIBRARY				       1-25-88


     Function 9	- Set Time

     On	Call:
       AH	 Function code 9.
       DX	 Unsigned 16-bit timer value.

     On	Return:
       AL	 Return	code.



     Function 10 (A Hex) - Get Time

     On	Call:
       AH	 Function code A (hex).

     On	Return:
       AL	 Return	code.
       DX	 Unsigned 16-bit timer value.







































				Page  4	- 3




     MIDI INTERFACE LIBRARY				       2-22-88


			    5.	PASCAL FUNCTIONS


     Since the functions are implemented as a "BIOS", it isn't hard to
     re-implement them for any language	that supports BIOS function
     calls. All	that's needed to do the	"port" is to provide function
     calls in the language that	do the BIOS call efficiently. For
     example, here's a set of Turbo Pascal functions that correspond
     exactly to	the C functions, and are implemented by	calling	the
     same BIOS that the	C library does.

     The functions that	follow constitute the interface	part of	a
     Turbo Pascal 4.0 "unit" specification, which we could implement
     as	the "MIDI" unit.

     function midi_putc	( b : byte ) : integer;

     function midi_getc	( var b	: byte;	var t :	word ) : integer;

     function midi_putmsg
			(
			var buf	     : string;
			    bufsize  : integer;
			var xmtsize  : integer;
			)	     : integer;

     function midi_getmsg
			(
			var buf	     : string;
			    bufsize  : integer;
			var rcvsize  : integer;
			var timestamp: word;
			)	     : integer;

     function midi_settempo
			(
			    speed    : word;
			var maxcount : word
			)	     : integer;

     function midi_settime ( t : word )	: integer;

     function midi_gettime ( var t : word ) : integer;

     function midi_init	: integer;

     function midi_end : integer;











				Page  5	- 1




     MIDI INTERFACE LIBRARY				       2-21-88


			   6.  FUTURE DIRECTIONS

     This section deals	with features that we might want to add	to the
     MIDI library at some time in the future, and reasons for adding
     (or not adding) them. There is also some discussion about how
     they might	be added.



     Active Sensing

     It	is reasonable to try to	keep management	of the Active Sensing
     message out of the	application. The driver	that implements	the
     MIDI library could, upon detecting	an incoming Active Sensing
     message, set itself into a	mode in	which it sends such a message
     every quarter second in the absence of any	other outbound
     traffic. (This is conceptually easy, and probably not difficult
     in	practice.)

     The above paragraph is an automatic capability, having no
     implications at the application program interface (except that
     Active Sensing messages need never	cross the interface). But some
     synthesizers might	require	such messages, even though the spec
     says that you have	to send	at least one if	you expect to receive
     them. One way around this is for the library to set the Active
     Sensing mode if it	sees an	Active Sensing message either inbound
     or	outbound. In this way, an application that knew	it needed to
     start up the Active Sensing feature could simply send an Active
     Sensing message.



     Filters

     As	I mentioned in Section 2, filtering MIDI messages (either
     outbound or inbound) is logically an application function,	and
     really doesn't belong in the driver. However, an efficiency
     argument might be made that it is advantageous to filter inbound
     messages in the driver. If	certain	popular	boards (e.g. - the
     MPU-401) do filtering, that lends weight to such arguments,
     especially	if many	applications use that feature of the board.

     The returns are not in on whether (or, if so, how)	filtering
     should be included	in the driver. If they are added, and if the
     argument for adding them is a pre-existence argument for some
     existing board, then the library functions	for dealing with
     filters should be compatible with the facilities provided by that
     board (while remaining as hardware-independent as possible).










				Page  6	- 1